## Slide 1: Flote Behavioral analysis by measurement of stereotyped movements in zebrafish
Harold A. Burgess Laboratory of Molecular Genetics

## Slide 2: Flote workshop
0. Overview of behavioral analysis
1. Image acquisition and storage (workshop and demo)
2. Flote: Single event analysis
3/4. Flote / Batchan: Batch tracking and analysis
5. Histo: Exploration of results
6. Misc., questions etc.

## Slide 3: Flote
1. Computational identification of maneuvers
2. High throughput behavioral analysis

## Slide 4: Flote: Rapid quantification of maneuvers
You: Record video
Flote: Compute curvature
Batchan: Classify maneuvers
Histo:Statistical analysis

## Slide 5: Flote: Rapid quantification of maneuvers In groups
Each stimulus, save 20 video sequences: 20 measurements
Expose each larvae to 5 stimuli: 100 measurements
Test larvae in groups of 30: 3,000 measurements
Experiment contains 10 groups: 30,000 measurements
n = 10... but each is the average of 3000 points

## Slide 6: Flote workshop
0. Overview of behavioral analysis
1. Image acquisition and storage (workshop and demo)
2. Flote: Single event analysis
3/4. Flote / Batchan: Batch tracking and analysis
5. Histo: Exploration of results
6. Misc., questions etc.

## Slide 7
Image acquistion and storage
Image acquisition - setting up a nice shot
Video acquisition - selecting a time window
Storing image stacks - optimizing throughput

## Slide 8
Image acquisition
Larval image size
Imaging area
512x512 pix = 35x35 mm
Larva:
~ 50 pixels

## Slide 9
Image acquisition
Contrast and focus
Depth: don't allow larvae to dive/rise out of focus!
Tolerant to a range of contrasts, lighting should be ok.

## Slide 10
Fair
Not manageable
No non-fish contrast elements in the middle (eg dirt) are ok.
Exception, regular grids are ok.
Image acquisition
Non-fish contrast elements
*

## Slide 11
Video acquisition
How many images per trigger
Number of frames:
- Startle responses: 100 frames after trigger
- Normal swimming: 400 frames per trigger
Camera
Stimulus
Timer
Frame rate: must be 1000 fps
(for kinematic analysis)
Prestimulus: Collect 10-30 images before the stimulus trigger to identify fish already swimming

## Slide 12
Storing images
Optimal file naming convention
A plate of larvae was tested with a sequence of 20 stimuli, with a recording window of 400 frames collected for each stimulus.
How to save the 8000 frames?
Use of a standard naming convention will:
1. Let Flote load files more quickly during tracking
2. Let you get maximum value out of the q&d statistics.

## Slide 13
Storing images
Optimal file naming convention
con_00a
Naming convention:
[Folder Name]_#####.jpg
- starts at zero (except Photron)
- number length not important
- correct mistakes with AF5
con_00a_0000.jpg
con_00a_0001.jpg
con_00a_0002.jpg
con_00a_0003.jpg
con_00a_0004.jpg
con_00a_0005.jpg
con_00a_0006.jpg
con_00a_0007.jpg
con_00a_0008.jpg
con_00a_0009.jpg
con_00a_0010.jpg
con_00a_0011.jpg
con_00a_0012.jpg
con_00a_0013.jpg
con_00a_0014.jpg
con_00a_0015.jpg
con_00a_0016.jpg
con_00a_0017.jpg
con_00a_0018.jpg
con_00a_0019.jpg
con_00a_7999.jpg

## Slide 14
Storing images
How to choose a folder name for easy analysis
c100_00a
Unique name for this plate of fish
Repeated tests: a to z
Condition:
concentration
100 uM
First plate tested
under this condition

## Slide 15
Storing images
How to choose a folder name for easy analysis
c000_00a
c000_00b
c000_01a
c000_01b
c000_02a
c000_02b
c100_00a
c100_00b
c100_01a
c100_01b
c100_02a
c100_02b
Each plate was tested twice
- Using a-z for multiple tests facilitates averaging
- Using common element for conditon facilitates averaging
Three plates tested per condition

## Slide 16
Storing images
Optimal structure of folders for fast analysis
1102_Startle
c00_00a
c00_00b
c10_00a
c10_00b
All recordings that constitute an experiment in a folder.
Subfolder names are all the same length.
(No need for folder names to be zero based)

## Slide 17
Storing images
Optimal structure of folders for fast analysis
Video
1102_Startle
1102_Fear
1103_Flash
1104_Phot
Convenience:
1. Folders sit in a network shared directory
2. All experiment folders are in a common directory
c00_00a
c00_00b
c10_00a
c10_00b

## Slide 18
Storing images
Format
JPEG
8-bit (greyscale)
75 % compression
Benchmark: 15 seconds per 1000 frames (512x512 pix)
Improve speed:
- Save to local drive
- Use PCI based (or streaming!) camera
- Regularly wipe and reformat drive

## Slide 19: Tracking overview Using Flote to track and analyze a video
1. Quick demo - single event analysis
2. What happens during tracking?
3. Step by step analyzing an event

## Slide 20: Tracking overview Five steps to analyze one video sequence
1. Select video directory
2. Load frames corresponding to trigger
3. Select configuration
4. Press track
5. Press analyze
[Demonstation: track set in spont directory]

## Slide 21: Tracking: What happens? 1. Follow larva from frame to frame
Particle tracking algorithm
- Find all the larvae in frame 1
- Position: the optical centroid
- Track: the position of each larva in all subsequent frames

## Slide 22: Tracking: What happens? 2. Estimate the curvature of the larva
Head orientation: Fit a bar from the head centroid along body
Body orientation: Fit a bar from the end of the head bar
Tail orientation: Fit a bar from the end of the body bar

## Slide 23: Tracking: What happens? 2. Estimate the curvature of the larva
Curvature
- Sum of angles between head/body and tail/body
Curvature time function
- Repeat for the larva over every frame

## Slide 24: Tracking: What happens? 3. Find the position of the eyes
Good
Excluded from analysis
Balance defect
Collision
Shmutz
- Greatly improves tracking by excluding non-fish elements
- For clean plates with rare collisions, is a good proxy for balance defects

## Slide 25: Analysis: What happens? 1. Make a lot of kinematic measurements
- Kinematics are in themselves useful for studying behavior
- Allows classification of the maneuver executed

## Slide 26: Analysis: What happens? 2. Classify the event using kinematics
Nothing (stationary)
O-Bend
SLC
R-Turn
Duration
Angular Velocity
C1 Angle
Something: use
kinematic information to classify

## Slide 27: Tracking: Stepwise
1. Load image stack
2. Adjust frame
3. Adjust head and tail parameters
4. Track - check curvature function
5. Setup behavioral parameters
6. Analyze

## Slide 28: Loading an image stack Selecting current video directory
Select current video directory
- Flote checks it contains suitable files
- Loads the first image in the directory
- Sets it as the working directory
Demonstation set: \workshop_video\spont\t50_e02a

## Slide 29: Using the folder browser
Problem: Browser seems to freeze after double clicking an image directory
Solution: Wait for a very long time.
Problem: Browser doesn't actually select the directory properly
Solution: Close zoom window and plot window

## Slide 30: Loading an image stack Selecting current video directory
If this is successful then
- Shows the current directory
- First image appears in the display
- Dialog window shows dimensions
Problem: Fails because image naming convention is not _0000.jpg
Solution: Toggle alphanumeric file order.
If not successful then message:

## Slide 31: Loading an image stack Loading the first group of frames
Once you have a current video directory load the first set of frames.
Note: Flote always refers to the first frame as frame 0
EVEN THOUGH!!! Photron will call it _00001.jpg
If directory contains only 1 trial, you can just use 'Load Whole Directory'
Depends on your experiment.
Generally
119 : for startle responses
399 : for normal swimming
999 : for dark flash responses

## Slide 32: Loading an image stack Loading subsequent sets of frames from same stack
Quickly load next/prev sets of frames
Quickly load a given trial number
eg: entering 10 here would load 1000-1099
Tip: frame numbers and trial number are down the bottom left corner.

## Slide 33: Loading an image stack Options during loading
Rotate/flip the image during loading. You should not usually do this.
For image stacks with non-standard naming (eg non Photron / Redlake / DRS).

## Slide 34: Video Playback
Play backwards / forwards
Current frame displayed
Show every Nth frame
- valuable for making videos
eg Original recording: 1000 frames
- set playback at 5
- output is 200 frames
- set movie maker to 25 fps
- movie is 8 seconds long
- original is 1 second long
- so your movie is 8x slower
Slide to pick a given frame

## Slide 35: Adjusting the frame Removing unwanted contrast elements
Frame (box)
Radius (circle)
Wells
Frame and Radius: exclude particles outside the border
Wells: tracks only the most 'fish-like' object in each well
- not necessary for tracking in a grid
- removes false fish produces by grid contrast

## Slide 36: Finding head and eye positions
- Experiment with Noise Size, Object Size and Bandpass button
- Experiment with Diameter, Density
- Experiment with Display  Head Shape
- Test the eye find parameters [density '400' = 4 on slider]
Tip: Restore the default settings with Configuration  Default

## Slide 37: Finding body curvature
- Experiment with segment length slider
- For normal tracking, never adjust segments=3 or max bend=220
- Aim to get the first bar at end of swim bladder
- Tip of tail is usually not trackable (contrast / verticality)

## Slide 38: Setup to tracking algorithms
Select/adjust head finding algorithms
Select/adjust curvature algorithms
When in doubt use:
- rapid tracking
- follow eyes
- orient line density
- low contrast

## Slide 39: Setup to tracking algorithms Head find options
Crocker algorithm for mass particle tracking
- Ignore, its slow
- Future potential for mass (1000s) tracking
If larva sometimes loses contrast
- eg Fast movement or stimulus artifact
- When particle lost, Flote reduces density thresh.
- Can be very very slow!
If larva moves very fast, expands search window
- Normal: 50 pixel square
- Broad: 100 pixel square
- More useful for xya analysis at 25 fps.

## Slide 40: Setup to tracking algorithms Eye find options
If checked, looks for eye positions throughput the video sequence, not just in the first frame
- Useful for measuring locomotor balance
- Optional because it does slow tracking down by about 25%, so if this is an issue and you don't care about balance, turn off.

## Slide 41: Setup to tracking algorithms Curvature find options
Point density:
- for very high contrast images
- often better for startle
Line density:
- usually more reliable

## Slide 42: Setup to tracking algorithms Curvature find options
Point density:
- for very high contrast images
- often better for startle
Line density:
- usually more reliable
- generally used with 'low contrast' option
Ellipse: for tracking eye movement in high res. images
Overlapping contours: for tracking blobs (flies)

## Slide 43: Track
Click
Watch
Tip: If you are loading, tracking and analyzing many videos manually, then use the File  Track on load feature to save clicking the button

## Slide 44: Track Track on load feature
Toggle so that loading a frame set causes Flote to automatically track it (without having to press Track)

## Slide 45: Analyze trial
Annotate video
Kinematics and Behavior
Time Series Data
Time Series Plot

## Slide 46: Analyze trial Annotating the video window
Toggle options on/off [experiment]
Generally the first six are checked
Note: None of these options affect kinematic analysis - they are display only!
Copies all display updates to 'C:\ftrack\images'
- very useful for making annotated movies
- remember to turn off when done!

## Slide 47: Tracking and display Saving the configuration
Frequently used tracking/display configurations can be saved and will then appear in the drop-down menu
- give the configuration a memorable name
- config files are in c:\ftrack\track_configs
- newly saved configurations only appear in the dropdown menu after you re-open Flote.
- Default is created by flote_setup program
Tip: The config file called 'Default' is loaded when Flote opens. You can write your preferred configuration over this by saving with the name 'Default'.

## Slide 48: Analyze trial Opening a zoom window
For a zoom of user defined area
- Hold down right mouse button and drag inside the display window.
- Area is then displayed in zoom window
- Zoom magnification depends on x-size
(ie drag a little horizontally, large zoom)
For a zoom of defined size
1. Select 100x or 200x
2. Hold right mouse button at top left
3. Drag across display window

## Slide 49: Analyze trial Selecting a larva for time series analysis
Annotation options
- Turns highlighting circle off
- Blocks annotate of other larvae
- Selected larva is horizontal in zoom window
Selecting a larva: Left click near its head.
- Larva selected becomes circled
Zoom selected larva: Right click on screen
- Zoom is always centered on selected larva
- Uncheck to turn feature off

## Slide 50: Analyze trial Time series analysis
Selecting a larva automatically opens the 'time series' window for frame by frame measurement of the selected larva
Clicking on a cell updates to the corresponding frame number in the video window.

## Slide 51: Analyze trial Time series analysis
Export contents of time series window to Excel (tab-separated file)
- if selected file exists, data is appended, not overwitten.
Tip: Limited screen real estate? Use Windows  Hide Time Series
Select which subset of parameters to display in the time series window
limits which frames are exported

## Slide 52: Analyze trial Graphical time series analysis
Plot button opens graphical interface to explore time series data
- Updated when you select a new larva
- Click on new column in time series window to select new plot parameter
Left click in plot window updates the display frame number
Left drag in plot window calculates the gradient
Change X and Y axis

## Slide 53: Analyze trial Kinematic and behavioral analysis
Maneuver identity
SLC
Other
Kinematics
... more about this later

## Slide 54: Analyze trial Kinematic and behavioral analysis
Maneuver identity
Startle
Other
Kinematics

## Slide 55: Analyze trial Maneuver identification
Maneuvers identified
SLC - Short Latency C-bend
LLC - Long Latency C-bend
Turn - Routine turn.
TurnO - O-bend.
Scoot - Slow forward swim.
Burst - Fast forward swim
J-Bend - J-Bend
Other classification
Swim - Movement initiated before stimulus
--- - Stationary
Excl - Exclude - not suitable for analysis
Flote can not yet recognize these maneuvers: Struggle, capture swim

## Slide 56: Analyze trial Kinematic analysis: c1 (first) bend

## Slide 57: Analyze trial Kinematic analysis: c2 (counter) bend

## Slide 58: Analyze trial Kinematic analysis: tailflips
1
2
3
4
5

## Slide 59: Analyze trial Kinematic analysis: Larvae excluded
e_sw - Frame # where larva started moving
e_oj - Frame # where error detected in curvature finding (rare)
e_ed - Frame # where larva too close to image edge
e_tk - Frame # where position tracking error (rare)
eyes - Number of eyes found (error if not in correct range)

## Slide 60: Flote workshop
0. Overview of behavioral analysis
1. Image acquisition and storage (workshop and demo)
2. Flote: Single event analysis
3/4. Flote / Batchan: Batch tracking and analysis
5. Histo: Exploration of results
6. Misc., questions etc.

## Slide 61: Batch tracking overview Analyzing thousands of trials - manually
You could just:
1. Next: Load next set of frames
2. Track: Track them
3. Analyze: Get behavioral data
4. Copy to spreadsheet
This would be tedious.

## Slide 62: Batch tracking overview Analyzing thousands of trials - in batch mode
Load video, track, save tracking files
Analyze tracking files in batch mode

## Slide 63: Batch tracking overview Tracking files
Produces tab-separated text files (Excel readable)
- files are in c:\ftrack directory
Position
Curvature
Tracking files are named track_XXXX_e##.sav
These are not easily readable.

## Slide 64: Batch tracking overview Analyzing thousands of trials - quickly
1. Adjust configuration by manually tracking a few trials
2. Setup Flote batch tracking
3. Run batch tracking until all video is tracked
4. Setup Batchan to analyze the tracking files
5. Analyze data using Histo program

## Slide 65: Flote batch tracking function Setting up the tracking configuration
Manually load and track first few trials
Check that it looks good by analyzing several larvae
Once configuration works nicely, save it as a config file
Configure batch tracking function

## Slide 66: Batch tracking overview Analyzing thousands of trials
1. Adjust configuration by manually tracking a few trials
2. Setup Flote batch tracking
3. Run batch tracking until all video is tracked
4. Setup Batchan to analyze the tracking files
5. Analyze data using Histo program

## Slide 67: Flote batch tracking function Preparing to batch track - input folder
Select directory containing a set of folders each with a video image stack
Structure of the experiment.
- Flote tries to remember based on the folder name 'xxxx_P/D01_xxxx'
Otherwise Flote guesses 120 or 400 frames
Example 1: Collect 120 frames for each of 40 startle stimuli = 4800 fr.
- should read 'each with 40 events of 120 frames'
Example 2: Collect 8 seconds of continuous recording during optomotor
- plan to analyze in 400 ms windows
- should read 'each with 20 events of 400 frames'

## Slide 68: Flote batch tracking function Preparing to batch track - output folder
Auto: creates output directory named after the video directory, but in the tracking folder.
Select a target directory
- needs to be manually created.

## Slide 69: Flote batch tracking function Preparing to batch track - other options
[Experiment with setting up batch track for all folders in workshop_video]
Filter: Only open video folders that match this field
Choose a tracking config file
- if none selected, Flote operates without changing the parameters in the main window
1
2
3
4

## Slide 70: Batch tracking overview Analyzing thousands of trials
1. Adjust configuration by manually tracking a few trials
2. Setup Flote batch tracking
3. Run batch tracking until all video is tracked
4. Setup Batchan to analyze the tracking files
5. Analyze data using Histo program

## Slide 71: Flote batch tracking function
Start batch tracking
- Ok to have multiple instances of Flote running
- Ok to use multiple computers in parallel so long as they point to a common network shared tracks folder
Camera
Lab PC
Your PC
Lab PC

## Slide 72: Flote batch tracking function
Current folder and position in list
Progress in this folder (inaccurate if tracking while experiment still runs)
Watch for 'incomplete' errors in the main Flote window.
- Error in file or folder name.
- Still being saved.
- Camera is not recording as many frames as you think it is.

## Slide 73: Flote batch tracking function Knowing when to stop
Exit immediately
Continue until all video is tracked, then search for any new video added that has not been tracked. Scans through all video folders and check all trials have a corresponding track_xxxx_.sav file
As for Run, but quit if no new video for an hour
Continue until all video is tracked, then quit
Hover to select mode
- patience! very slow responsiveness
Tip: Do not Run all night because this is not so good for your hard drives

## Slide 74: Batch tracking overview Analyzing thousands of trials
1. Adjust configuration by manually tracking a few trials
2. Setup Flote batch tracking
3. Run batch tracking until all video is tracked
4. Setup Batchan to analyze the tracking files
5. Analyze data using Histo program

## Slide 75: Batchan: analyzing track.sav files Example experiment
Example - Test the effect of hot water on spontaneous movement
3 control plates (add 28C water)
3 test plates (add 40C water)
Test each plate once like this:
Baseline (4 sec)
Response (4 sec)
Add the 28 or 50 C water

## Slide 76: Batchan: analyzing track.sav files Combining tracking files
Each plate was recorded for 4 seconds before test water added, then 4 seconds after water added.
- Each 4 seconds was tracked as ten 400 ms long trials
So we have 20 tracking files for each plate.
Plate 1: Folder was t028_00a so tracking files are:
track_t028_00a_e00 to track_t028_00a_e19
Plate 2: Folder was t028_01a

## Slide 77: Batchan Combining tracking files
For each plate tracking files e00-e09 contain baseline movement, e10-e19 contain stimulus response
Baseline
Stimulus

## Slide 78: Batchan Combining tracking files
Baseline
Question 1: How frequently do larvae initiate different maneuvers during baseline and stimulus conditions?
Load all 10 tracking files (e00-e09), run the behavior analysis routine and then
- Count total number of analyzable larvae
- Count number of Scoot, Turn, J-bend etc occuring
% Scoot = 100 x [total # scoots observed] / [total # larvae]
% Turn = 100 x [total # turns observed] / [total # larvae]
% Jbend = 100 x [total # jbends observed] / [total # larvae]
etc
So: in this case there are 10 trials per set.

## Slide 79: Batchan Setting up batchan
[Demonstration - analyze the tracks in the workshop_tracks folder]

## Slide 80: Batchan
Input folder
Output folder
Names
Analysis Method
Image subsets
Trial subsets
Grids
Start analysis

## Slide 81: Batchan Selecting input folder
Browse to a folder containing a stack of track_XXXX.sav files.
Only include tracking files which match this field.
Example: Tracking files are named track_con_00a.sav
track_con_01a.sav
track_con_02a.sav
track_exp_00a.sav
track_exp_01a.sav
track_exp_02a.sav
Enter 'con' in filter field to only analyze the control videos.

## Slide 82: Batchan Selecting output folder
Browse
to folder
If checked, do not write over any files existing in the output folder, instead, add the new analysis results to the end of existing files.
Make a sub-folder in the tracking folder
Automatically given prefix of the name of the analysis
algorithm
Tip: leave the output folder field blank and batchan will create an output folder based on the number of trials per set.

## Slide 83: Batchan Naming the trial sets
We need to give this set a unique name in the output file. The name is by default identical to the name of the first tracking file in the set.
Example, for the set of tracking files starting with:
track_t028_00a_e00.sav
Baseline
track_t028_00a_e00
base [all sets have the same name!]
base_t028_00a_e00
t028_00a_e00_base

## Slide 84: Batchan Trials per set
How many tracking files should be combined into a single measurement?
For the example, it would be 10 trials per measurement.
Sometimes it is useful to use a smaller number, eg 1, 2, 5 - to see if there is a trend in the data.
Entering * in this field combines all tracking files into a single set.
Baseline

## Slide 85: Batchan Using subsets of trials
Baseline
Stimulus
For baseline activity, we only want to analyze tracking files 00-09
equivalent
If field is blank, batchan will go through the whole directory and clump tracking files according to the number of trials per set.
Eg. Trials per set = 10
track_t028_00a_e00 .... track_t028_00a_e09
track_t028_00a_e10 .... track_t028_00a_e19
track_t028_01a_e00 .... track_t028_00a_e09

## Slide 86: Batchan Using subsets of trials
Also useful when stimuli are in a pseudorandom order.
Enter the string once into the trial number field, then use
Trials  Save Subset to have it saved in the dropdown menu
(but it only appears next time you open batchan).
Give the trial subset an easy to remember name!
Subsequently just select the name from the dropdown menu and the sequence is entered into the trial numbers field
Even # and Odd # : enter 0,2,4,6 etc or 1,3,5,7 etc

## Slide 87: Batchan Using subsets of trials
Common experiment: baseline and stimulus, presented in a pseudorandom order.
Two quick access presets for an experiment with 40 trials.
2Set:A - 0,3,5,6,7,11,12,15,16,18,20,21,22,25,28,30,33,34,35,39
2Set:B - 1,2,4,8,9,10,13,14,17,19,23,24,26,27,29,31,32,36,37,38

## Slide 88: Batchan Analyzing individual fish in a grid
Enter grid size here 3x3 etc.
If there are multiple fish in a grid element, batchan says no fish are found in that element.
Real world
Position in Flote
Check how position correlates to number (depends on how camera inverts image and how software saves image).

## Slide 89: Batchan: analyzing track.sav files Analyzing individual fish in a grid
Which fish to analyze. NOT the same as the fish number given during tracking by Flote. Refers to the grid position.
Batchan automatically appends -f1, -f2 etc to the end of the name so you know which fish was analyzed.
Check box to automatically go through the whole grid.
- Batchan will enter 1, 2, 3, etc into the fish number box and analyze each grid position

## Slide 90: Batchan: analyzing track.sav files Select analysis algorithm
Best for analyzing %SLC
Best for analyzing everything else
Best for xya analysis
Threshold value used by algorithm for scoring movement versus no movement.
For startle response analysis, best from 8-16 (depending on noisiness and resolution)

## Slide 91: Batchan: analyzing track.sav files Open behavior parameters setup
Displays current values

## Slide 92: Batchan Behavior parameters setup
Analyze subset of frames
Ignore: for kinematic mutants
Ignore: for xya analysis

## Slide 93: Batchan Behavior parameters setup
Stimulus time: for excluding larvae that are moving before the stimulus
If you have no stimulus still set this to ~10.
It is needed to exclude larvae already moving at the beginning of the video window.
We can't identify the maneuver without seeing the initiation.

## Slide 94: Batchan Behavior parameters setup
Minimum, Maximum number of eyes a particle can have to be identified as a larvae.
2,2 - normal setting, allows measuring turn direction
1,2 - include larvae with balance defect, a common mutant phenotype.
Balance defect
Collision
Shmutz

## Slide 95: Batchan Behavior parameters setup
For startle response analysis.
Generally %SLC is reliable even if there are subsequent tracking errors.

## Slide 96: Batchan Behavior parameters setup
Usually leave checked to exclude larvae already moving before the stimulus.
Occasionally for startle responses this can be unchecked - for example if you don't care about movement initiation frequency, just directionality.

## Slide 97: Batchan Behavior parameters setup
Larvae that aren't swimming, but are floating forward are usually excluded.
This usually makes no difference.

## Slide 98: Batchan Behavior parameters setup
Only consider it an SLC response if it has high performance kinematics.
This can be useful if you don't know when the stimulus arrives - use kinematics to identify the SLC events.

## Slide 99: Batchan Behavior parameters setup
The most reliable way to identify SLC responses - they are initiated in a very narrow time window (specified below).

## Slide 100: Batchan Behavior parameters setup
Configurations to quickly access commonly used settings.
Stored in c:\ftrack\behavior_configs

## Slide 101: Batchan Obscure parameters
Normal method for calculating initiation frequency:
LLC = 100 x [total # LLC observed] / [total # larvae]
Check to get LLC = [total # LLCs observed]
Normal method for calculating initiation frequency removes larvae that executed a SLC from the pool
ie [tot # larvae] = [all analyzable larvae] - [those that executed SLC]
Rationale: important for calculating real rate of LLC responses.

## Slide 102: Batchan Configuration files
Not necessary to go through setting parameters each time.
Saved configurations are in c:\ftrack\analysis_configs
Does NOT effect the behavior parameter settings.

## Slide 103: Batchan Run analysis
When everything is in place - press Run button.
The name of each set
Tracking files combined for that set.
During analysis a window pops up showing:

## Slide 104: Flote workshop
0. Overview of behavioral analysis
1. Image acquisition and storage (workshop and demo)
2. Flote: Single event analysis
3/4. Flote / Batchan: Batch tracking and analysis
5. Histo: Exploration of results
6. Misc., questions etc.

## Slide 105: Batchan Output files
Initiation frequency and direction.
Kinematic parameters for every movement episode analyzed.
Position, orientation measurements.
TIP: All are tab-separated text files easy to open in Excel

## Slide 106: Batchan Output files: c1_analysis.trk
Number larvae identified
Number larvae analyzable
% Excluded for each reason (many larvae are exluded for multiple reasons)

## Slide 107: Batchan Output files: c1_analysis.trk
% Any movement
Initiation frequency for maneuvers

## Slide 108: Batchan Output files: c1_analysis.trk
Left/Right direction of maneuvers
eg Obend(r) = "The proportion of Obends made in a rightward direction"
-NaN: can't be calculated (bursts=0)

## Slide 109: Batchan Output files: c1_analysis.trk
# - relative to orientation
#, # - relative to (x,y) position
+100
0
-100
always towards
no bias
always away
Bias: Directionality of maneuvers relative to a target point or orientation

## Slide 110: Batchan Output files: summary.trk
Contains position, orientation and kinematics of every movement identified.
The name of the trial set appended by the # of the tracking file
The number Flote gave the fish during tracking.
Codes for type of maneuver
0 - No movement (not usually reported)
1 - SLC
2 - LLC or Routine Turn
3 - Scoot
4 - Burst
5 - Obend
7 - [Unidentifiable]
8 - Jbend

## Slide 111: Histo
Note: Always confirm findings in histo using a real statistics program
Press.
Select file to analyze.

## Slide 112: Histo The histo windows
Graphing Window
Print
Set
Members

## Slide 113: Histo Types of graph

## Slide 114: Histo Types of graph

## Slide 115: Histo Defining sets of groups
In histo, a set is a clump of measurements who need to be averaged.
You instruct histo on what measurements go together based on pattern matching.
Baseline: Combined into a single data line called:
base_t028_00a_e00.sav
In this experiment, we want to compare the average baseline activity to the average stimulus activity and therefore need to find the average and st. dev. of
base_t028_00a_e00.sav
base_t028_01a_e00.sav
base_t028_02a_e00.sav
We could use 'base_t028' to distinguish from 'flow_t028'

## Slide 116: Histo Defining sets of groups
We could use 'base_t028' to distinguish from 'flow_t028'.
- Ignore the last 8 characters of the name
Method 1. Select from dropdown menu
Method 2. Open dialog box and click where you want to match

## Slide 117: Histo Checking the sets contain the right groups
Dropdown menu contains all the sets made according to your criterion.
Selecting a set causes:
Graph window: set is highlighted
Subsets window: groups in the set are listed. Check!

## Slide 118: Histo Bar plots
Bars show mean, st. dev and N for the four sets
Parameter being analyzed
Click once on another bar to make it the selected set

## Slide 119: Histo Bar plots
Move bar left/right
Toggle Stnd Dev / SEM

## Slide 120: Histo Selecting a parameter to analyze
Dropdown menu contains all the parameters (column headers) in the file.
Select previous or next parameter for analysis

## Slide 121: Histo Bar plots
Toggle
ANOVA
display
Toggle
t-test
display
Hold left mouse button down and drag between columns to compare them by t-test

## Slide 122: Histo Bar plots
Toggle paired t to make the comparison between selected columns a pairwise t-test
Select blank in sets dropdown menu to have no set selected
Drag across whole graph to reset bar comparisons

## Slide 123: Histo Bar plots
Shows t-tests between the two parameters for each set.
Select a parameter in the 2nd parameter dropdown menu to plot both in one graph

## Slide 124: Histo Histogram mode: for kinematic analysis
Summary.trk file to look at kinematic parameters
Adjust binning

## Slide 125: Histo Histogram mode
Black - all data points loaded
Blue - selected set
Drag across to select a range
Orange - selected range for selected set
Select range: 1 or 2 std dev from mean
Select all points outside the selected range.

## Slide 126: Histo Histogram mode
Discard all non selected points
Discard the currently selected group

## Slide 127: Histo Histogram mode
Show only selected set
Show as relative frequency distribution (0-100%)
Preset view buttons: Select parameter and binning.

## Slide 128: Histo Histogram mode
'Resp' - Codes for the type of maneuver
Selecting a maneuver masks out data belonging to a different maneuver.

## Slide 129: Histo Analyzing a selected range
Select a range in the histogram
Example: Angle > 41
Select another parameter. The orange still highlights the same data points.

## Slide 130: Histo Analyzing a selected range
Select a range in the histogram
Example: Angle > 41
Bar graph mode: select a (different) parameter in both the primary and secondary dropdown menus.
Compares mean values for entries
- Black: Angle < 41
- Orange: Angle > 40

## Slide 131: Histo Comparing kinematics
Step 1.
Make a set for each plate and condition tested to find the average values for movement events.
Step 2.
Select a maneuver to analyze (there is no point taking the mean across all maneuvers).

## Slide 132: Histo Comparing kinematics
Step 3.
Save the means for each of the 12 sets.
- Creates a new file summary_means.trk
- Automatically loads the new file.
Step 4.
Define new sets using pattern matching to create four sets:
- base_t028
- base_t045
- flow_t028
- flow_t045
Each has three data points in it.

## Slide 133: Histo Comparing kinematics
Step 5. - Compare groups with bar graph

## Slide 134: Histo The print window
Left click: copies the graph window at the position
Right click: copies the graph window at the position, but at 0.25x the size.
Menu - options for output or clearing.

## Slide 135: Histo The subset window
Value1 (Value2)
Value1 = the value for the currently selected parameter
Value2 = the value for the parameter in which a range has been selected.
Toggle off group names to see values only (useful for copy / paste into Excel)
Delete the item where the cursor is placed.

## Slide 136: Flote workshop
0. Overview of behavioral analysis
1. Image acquisition and storage (workshop and demo)
2. Flote: Single event analysis
3/4. Flote / Batchan: Batch tracking and analysis
5. Histo: Exploration of results
6. Misc., questions etc.

## Slide 137: Flote directory c:\ftrack
Back this directory up regularly!
If in doubt where a file is - look here.

## Slide 138: AF5 Utility Batchan rename large file stacks
Invaluable utility by Alex Fauland.

## Slide 139: Annotating stimulus time on display
Check Display  Annotate  Stimulus
Check Display  Annotate  Main Window
Use Display  Annotate  Setup Stimulus
and enter the first and last frame of the stimulus
Note: Similar method to annotate the zoom window

## Slide 140: Annotating time series on display
Check Display  Annotate  Time Series
Check Display  Annotate  Main Window
Use Analysis  Select Analysis Parameters
and make sure that only the parameter to be plotted is checked
Select a larva by left clicking on it